Pictures of APR AS-105940 installation on 2009 Lancer ES.

It is a simple installation but you will need two additional bolts not included with the spoiler. You will need two 2.5” ¼ bolts. Just bring one of the other bolts to Home Depot or Lowes and get two that are 2.5” long and the same thread. You will need them for the middle hole of the bracket. When you drill the hole, you must drill through the trunk and through the support metal on the inside. That is the reason for the length. Once the spoiler is installed and the nuts are tightened use a hack saw and the cut the passenger side bolt a little so it doesn’t hit the rubber lining around the edge of the trunk when you close it.

You can see the middle bolt is the one mentioned to cut. The top bolt fits into the existing spoiler hole and the lower bolt is drilled where there is already a circle on the trunk frame. We drilled the lower hole and then used the rubber seal for the base of the spoiler to mark the middle hole and then drilled it. Again, it is not difficult.

I plan to paint the head of the silver bolt you see black.

Hope this helps if someone else has questions.

Brian